This document describes the necessary steps to setup, prepare and run the Eros model and visualize its outputs from within Matlab.

Test platforms:
- Win 10 64-bit, AMD Ryzen 7 2700X Eight-Core Processor 3.70 GHz, Matlab R2017a
- Win 10 64-bit, Intel Core i7-3770 Quad-Core Processor 3.70GHz, Matlab 2018b

1. Set up Eros and run example experiment
  1. Download program and extract files
  2. Add files in the mfiles-folder to the Matlab path
  3. Open eros_template.m, scroll to line ~53 and change directory to where the bin-folder resides
  4. Cd to ProjectFolder and run eros_template.m. This executes the example experiment of a flat, inclined slope (~5 minutes computation time on Ryzen 7, ~10 min on i7)
  5. Change directory to the folder where the results were written to
     [e.g. Results\inflow(10).initial_sediment_stock(0.1).sediment_threshold(4)]
  6. Use erosinfo.m to show some variables written during model execution, e.g.:

     doc erosinfo shows a list of variable options
     B = erosinfo(‘topo’);	plots the average elevation as a function of time
     B = erosinfo(‘all’); shows all relevant data in a 3-by-3 subplot.
  7. With erosanimation.m you may:
     B = erosanimation(‘water’); show a 2d-animation of water flow and store the frames in B,
     B = erosanimation('sediment','mode','average'); show mean sediment thickness evolution,
     B = erosanimation(‘topo’,’mode’,’movie3’); show a 3d-animation of topographic evolution.
  8. The function frames2gif.m:
     frames2gif(B,’filename.gif’,0.1); saves an animated gif from frames in B created with erosanimation with a delay between frames of 0.1 seconds.
  9. To access an individual output file:

     F = grd2GRIDobj(filename_with_extension);
2. Prepare inputs for real topography and run model. In eros_template.m you may:
  1. specify the
    - topographic base (.alt),
    - the source/sink raster (.rain),
    - the sediment thickness distribution (.sed),
    - the water discharge on the topography (.hum),
    - the water level on the topography (.water),
    - a map of spatially variable erodability (.erode)
    - and a map of spatially variable manning coefficient (.manning).
Note: Only the first two inputs are required. The others are optional.
  1. change model parameters, output directory/name and the variables to write,
  2. write argument files for Eros.exe and
  3. start execution of Eros from within Matlab.